Proposed FDC Cathode Skin Tensioning Process

- Determine force on skin from the electric field. (Simon)

- Determine allowable deflection of Cathode plane at center (what is allowed?)

- Convert field force to point force at center of cathode plane (FEA model or hand calc. using known Kapton stiffness modulus)

- Calibrate a dial indicator in the deflection range determined range (force vs. deflection).

- Setup cathode plane in tensioning device with twice the approximate expected deflection (sag*).

- Setup dial indicator  over cathode plane until just touching the plane

- Tension the plane until indicator moves the desired amount (equal to allowed deflection from step 2).

*The amount of initial sag may have to be experimented with to get the desired results.